###### Konica Minolta DiMAGE Z20 Digital Camera

###### Specifications

| Number of effective pixels | Approximately 5.0 million |
| --- | --- |
| CCD | 1/2.5-inch interline primary-color CCD Total pixels: Approximately 5.2 million |
| Camera sensitivity | Auto and 50,100, 200, and 320 ISO equivalents |
| Focal length | 6 - 48mm (35mm equivalent: 36 – 290mm) |
| Lens construction | 11 elements in 9 groups |
| Maximum aperture | f/3.2 – f/3.4 |
| Minimum focus distance | Wide: 1.6ft (0.5m) from front of lens Telephoto: 4.9ft (1.5m) from front of lens |
| Minimum macro distance | Macro Mode: Wide: 0.4 in. (0.01m) Tele: 23.6 in. (0.6m) |
| Maximum magnification | 0.24x Equivalent to 1.5x in 35mm format |
| Area covered at maximum magnification | Approximately 1.0 x 0.7 in. (25 x 18mm) |
| LCD monitor | 1.5-inch low-temperature polysilicon TFT color Total number of pixels: 113,000 Automatic monitor amplification |
| Viewfinder type | Electronic Viewfinder |
| Field of view | Viewfinder: Approximately 98% LCD monitor: Approximately 100 % |
| Display-mode switch | Viewfinder display, LCD-monitor display Switch Finder system allows the monitor to be viewed directly or through the viewfinder. |
| Diopter control | – 3 ~ +1m-1 |
| Eye relief | 18.8mm |
| Shutter | CCD electronic shutter and mechanical shutter |
| Shutter speed range | 4 - 1/2000 |
| Autofocus system | Rapid AF: a combination of a passive AF sensor with the video AF system |
| Autofocus areas | 3-Point Wide Focus Area Spot focus areas with Focus Area Selection |
| Focus modes | Single-shot AF, Continuous AF with predictive focus control, Full-time AF, Manual focus. |
| Focus lock | By pressing shutter-release button partway down. |
| Metering | Multi-segment, Center-weighted, Spot |
| Multi-segment metering | 256 segments |
| Exposure modes | Programmed AE, Aperture priority, Shutter priority, Manual |
| Digital Subject Programs | Automatic (Portrait, Sports action, Landscape, Sunset, Standard) Manual (Portrait, Sports action, Landscape, Sunset, Night portrait.) |

| Exposure compensation | ±2 EV in 1/3 EV increments |
| --- | --- |
| AE lock | By pressing shutter-release button partway down |
| Flash metering | Pre-flash TTL |
| Flash range | Wide: Approximately 1.6 – 15.1 ft. (0.5 – 4.6 m) from front of lens Telephoto: Approximately 4.9 – 15.1ft. (1.5 – 4.6 m) from front of lens (Camera sensitivity: auto) |
| Flash modes | Autoflash, Autoflash with red-eye reduction, Fill flash, Flash cancel, Slow-shutter sync. Autoflash not available with aperture priority, shutter priority, and manual exposure modes. |
| Flash recycling time | Approximately 5 seconds |
| Flash compensation | ± 2 EV in 1/3 EV increments |
| Flash-sync speeds | All shutter speeds |
| Continuous advance | Frame per second (Approximately) * Actual speed may vary depending upon the subject and camera settings. Approximate number of frames that can be captured at one time with the continuous-advance drive modes: continuous advance 2560x1920 2048x1536 1600x1200 640x480 Fine 3 frames 3 frames 5 frames 28 frames Standard 4 frames 7 frames 11 frames 45 frames Economy 9 frames 13 frames 20 frames 64 frames * Actual number of images may vary depending upon the subject and camera settings. |
| Progressive Capture | Stores images from the latest frame captured with the continuous advance. Maximum number of images that can be recorded with the Progressive Capture mode: Maximum 6 frames (Approximately 1 frame per second) |
| Exposure bracketing | Three frame bracket in 0.5, 0.3 EV increments |
| Self-timer | Approximately 10 seconds, 2 seconds |
| Movie | Recording time dependent on memory card capacity, image size, and frame rate. Frame rate: 15 frames per second (640x480, 320x240) 30 frames per second (320x240) Movie frame capture, Night movie (automatic selection or disabled) |
| White balance control | Automatic, Preset (Daylight, Cloudy, Tungsten, Fluorescent, Flash), Custom |
| Digital Effects Control | Contrast compensation, Sharpness |
| Contrast compensation | Three levels (Low, Normal, High) |
| Sharpness settings | Three levels (Soft, Normal, Hard) |
| Color modes | Natural Color, Vivid Color, Black and white, Sepia |
| Digital zoom | Maximum 4x in 0.1x increments |

| Languages | Japanese, English, Germany, French, Spanish, Chinese (Simplified character), Italian, Swedish |
| --- | --- |
| Copy function | To copy single or multiple images 1).Card to card 2).Card to internal storage 3).Internal storage to card |
| E-mail Copy function | Creates a compressed 640x480 JPEG image for transmission. |
| Date imprinting | Year/month/day (Format can be changed.) Imprinting can be disabled |
| Key customization | The function activated by the flash-mode button can be changed. |
| Image-quality modes | Fine, Standard, Economy |
| Number of recorded pixels (Still images) | 2560x1920, 2048x1536, 1600x1200, 640x480 |
| Number of recorded pixels (Movie clips) | 640x480, 320x240, |
| Storage capacity | Approximate storage capacity of a 14.5MB internal storage: Still images 2560x1920 2048x1536 1600x1200 640x480 Fine 6 frames 9 frames 14 frames 71 frames Standard 11 frames 17 frames 28 frames 103 frames Economy 22 frames 33 frames 48 frames 155 frames Movie clips 640 x 480 320 x 240 30 fps - 21 seconds 15 fps 27 seconds 43 seconds Approximate storage capacity of a 64MB SD (Secure Digital) Memory Card: Still images 2560x1920 2048x1536 1600x1200 640x480 Fine 25 frames 38 frames 61 frames 297 frames Standard 49 frames 74 frames 117 frames 430 frames Economy 94 frames 138 frames 203 frames 645 frames Movie clips 640 x 480 320 x 240 30 fps - 1minute 31 seconds 15 fps 1 minute 56 seconds 3 minutes 3 seconds * Actual number of images may vary depending upon the subject and memory card used. |
| File formats | JPEG, Motion JPEG (MOV), DCF 2.0-compliant, DPOF- compliant (Supported by printing functions in version 1.1), Exif 2.2 |
| Folder name formats | Standard, Date |

| Printing output control | Exif Print, PRINT Image Matching III, PictBridge |
| --- | --- |
| Recording media | SD (Secure Digital) Memory Cards, MultiMediaCards, Internal storage (approximately 14.5MB) |
| Computer interface | Full-speed 12Mbps data transfer with USB 2.0 compatible computer |
| AV output | NTSC, PAL (selected on the camera) |
| Batteries | Four AA batteries: Alkaline, Ni-MH |
| Battery performance (Playback) | Approximate continuous playback time: 700 minutes with Alkaline batteries. |
| Battery performance (Recording) | Approximate number of recorded images: Approximately 450 Conforming to CIPA ( included AA alkaline batteries and SD memory card) |
| External power source | 6V DC with specified AC adapter (sold separately) |
| Dimensions (WxHxD) | 4.3 x 3.2 x 3.7 in. (109 x 82 x 94 mm) |
| Weight | Approximately 10.6oz. (300g) without batteries or recording media |
| Operating temperature | 32-104°F (0-40ºC) |
| Standard accessories | Neck Strap NS-DG800, Lens Cap LF-243B, Video Cable VC- 400, USB Cable USB-3, DiMAGE Viewer CD-ROM, Four AA, Alkaline batteries |
| Optional accessories | AC Adapter AC-11, Camera Case CS-DG1000, Leather Neck Strap NS-DG1000, Wide-angle Converter ZCW-200 |

System Requirements

The following operating systems are compatible with the camera: IBM PC/AT compatible

computers with Windows XP Home, Windows XP Professional, Windows Me, Windows 2000

Professional, Windows 98*, or Windows 98 Second Edition* and with a USB port as standard

interface.

Apple Macintosh computers with pre-installed Mac OS 9.0 – 9.2.2, Mac OS X v10.1.3 – 10.1.5,

and v10.2.1 – 10.2.8, v10.3-10.3.6 and with a USB port as standard interface.

• The computer and operating system must be guaranteed by their manufacturers to support

USB interface.

• Problems may be encountered depending on what other USB devices are being used in parallel

with this product.

• Only a built-in USB port is supported. Problems may be encountered when the camera is

connected to a USB hub.

• Normal operation may not be possible even when all the system requirements are met.

* Users with Windows 98 and Windows 98 Second Edition must install dedicated driver software included in the DiMAGE Z20 package.

Specifications and system requirements are subject to change without notice.

#   #   #

DiMAGE, CxProcess are trademarks or registered trademarks of KONICA MINOLTA Photo

Imaging, Inc. Windows is either a registered trademark or a trademark of Microsoft Corporation

in the United States and/or other countries. Macintosh is a trademark or registered trademark of

Apple Computer Inc. Other corporate names and product names are trademarks or registered

trademarks of their respective companies.