##### Konica Minolta DiMAGE G600 Digital Camera

##### Specifications

| Number of effective pixels | 6.0 million |
| --- | --- |
| CCD | 1/1.76-type interline primary-color CCD Total pixels: 6.40 million |
| Camera sensitivity | Auto, ISO 50, 100, 200, 400 equivalents |
| Focal length | 8 – 24mm (35mm equivalent: 39 - 117mm) |
| Lens construction | 7 elements in 6 groups |
| Maximum aperture | f/2.8 – f/4.9 |
| Minimum focus distance | Wide: 1.6 ft. (0.5 m) from front of lens Telephoto: 2.6 ft. (0.8 m) from front of lens |
| Minimum macro distance | Wide: 2.4 in. (6 cm) from front of lens Telephoto: 19.7 in. (50 cm) from front of lens |
| Viewfinder type | Optical real-image zoom viewfinder |
| Monitor LCD | 1.5 inch (3.8cm) TFT color monitor Total number of pixels: 117,000 |
| Shutter | CCD electronic shutter and mechanical shutter |
| Shutter speed range | Programmed AE: 1 - 1/2000 second Manual exposure mode: 15 - 1/1000 second |
| Autofocus system | Video AF |
| Metering | Center-weighted average, Spot |
| Exposure modes | Programmed AE, Manual |
| Exposure compensation | ±1.5 EV in 0.3 increments |
| Flash range | Wide: Approximately 1.6 – 9.9 ft. (0.5 – 3.03 m) Telephoto: Approximately 2.6 – 5.7 ft. (0.8 – 1.7 m) |
| Flash/Shooting modes | Autoflash, Autoflash with red-eye reduction, Fill-in, Off, Slow-sync, Macro-photo, Distant view, Self-timer, Fixed focus |
| Continuous advance | Available |
| Self-timer | Approximately 10 seconds, 3 seconds |
| Movie recording | Recording time: Maximum 30 seconds with monaural audio Frame rate: 15 frames per second |
| Audio recording | Maximum 30 seconds of audio can be recorded with and without an image. Audio can be recorded and attached to a playback image. Monaural audio only. |
| White-balance control | Automatic, Preset (Daylight, Cloudy, Tungsten, Fluorescent) |
| Contrast compensation | Five levels |
| Color saturation compensation | Five levels |
| Sharpness settings | Five levels |
| Color balance | Five levels for each RGB channel |
| Color modes | Color, Black-and-white, Sepia |
| Digital zoom | 2x, 3x |
| Copy function | To copy images and audio between memory cards. |
| Resize | To VGA (640x480) from 2816x2112, 2272x1704, or 1600x1200 size images for transmission. To QVGA (320x240) from 2816x2112, 2272x1704, 1600x1200, or 640x480 for transmission. |
| Compression modes | Fine, Normal |
| Number of recorded pixels (Still images) | 2816 x 2112, 2272 x 1704, 1600 x 1200, 640 x 480 |
| Number of recorded pixels (Movie clips) | 320 x 240 |
| Storage capacity | Approximate storage capacity of a 16MB SD (Secure Digital) Memory Card: |
|  |  | 2816x2112 | 2272x1704 | 1600x1200 | 640x480 |
|  | Fine | 5 frames | 8 frames | 16 frames | 66 frames |
|  | Normal | 8 frames | 16 frames | 32 frames | 133 frames |
|  | Movie clip | 30-second clips |
|  | * Movie clips recorded with audio. * Actual number of images may vary depending upon the subject and memory card. |
| File format | JPEG, Motion JPEG (AVI), WAVE DCF 1.0 -compliant DPOF-compliant (Supported by printing functions in version 1.1) Exif 2.2 |
| Printing output control | Exif Print, PictBridge |
| Recording media | SD (Secure Digital) Memory Cards, MultiMediaCards, Memory Stick |
| Computer interface | Full-speed 12Mbps USB |
| Battery | One NP-600 lithium-ion battery |
| Battery performance (Playback) | Approximate continuous playback time: 180 minutes |
| Battery performance (Recording) | Approximate number of recorded images: 160 frames Conforming to CIPA (included AA alkaline batteries, included SD memory card ) |
| External power source | 4.2 V DC with specified AC adapter (sold separately) |
| Dimensions (WxHxD) | 3.7 x 2.2 x 1.16 inches (94 x 56 x 29.5mm) |
| Weight | Approximately 6.88 oz. (195g) without batteries or recording media |
| Operating temperature | 32-122°F (0-50ºC) |
| Standard accessories | Neck strap NS-DG130, USB cable USB-800, 16MB SD (Secure Digital) Memory Card, Lithium-ion Battery NP-600 Lithium-ion Battery Charger BC-600U, DiMAGE Viewer CD-ROM |
| Optional accessories | AC Adapter AC-8U |

Minimum System Requirements

IBM PC/AT compatibles:

Computers:	IBM PC/AT compatible computers with pre-installed Windows XP Home, Windows XP Professional, Windows Me, Windows 2000 Professional, Windows 98*, or Windows 98 Second Edition* and with a USB port as standard interface.

RAM:	16MB of RAM (32MB or more recommended)

Monitor:	640x480 monitor capable of displaying 32,000 colors

Others:	CD-ROM drive

Apple Macintosh Computers:

Computers:	Apple Macintosh computers with pre-installed Mac OS 9.0-9.2.2, and Mac OS X v. 10.1.3-10.1.5, v. 10.2.1-10.2.8, v. 10.3-10.3.2 and with a USB port as standard interface.

CPU:	PowerPC

RAM:	16MB of RAM (32MB or more recommended)

Monitor:	640x480 monitor capable of displaying 32,000 colors

Others:	CD-ROM drive

•	The computer and operating system must be guaranteed by their manufacturers to support USB interface.

•	Problems may be encountered depending on what other USB devices are being used in parallel with this product.

•	Only a built-in USB port is supported. Problems may be encountered when the camera is connected to a USB hub.

•	Normal operation may not be possible even when all the system requirements are met.

*	Users with Windows 98 and Windows 98 Second Edition operating systems must install dedicated driver software included in the DiMAGE G500 package.

Specifications, accessories and system requirements are subject to change without notice.

#   #   #

Minolta and DiMAGE are trademarks or registered trademarks of Konica Minolta Camera, Inc.

Windows is either a registered trademark or a trademark of Microsoft Corporation in the United States and/or other countries. Macintosh is a trademark or registered trademark of Apple Computer Inc. All other brand and product names are trademarks or registered trademarks of their respective owners.