Konica Minolta DiMAGE X60 Digital Camera

Specifications

| Number of effective pixels | Approximately 5.0 million |
| --- | --- |
| CCD | 1/2.5-type interline primary-color CCD Total pixels: 5.4 million |
| Camera sensitivity | Automatic (between ISO 50 - 160 equivalent), ISO50, 100, 200, 400 |
| Focal length | 6.3 - 18.9 mm (35mm format equivalent: 38 - 114 mm), |
| Lens construction | 11 elements in 9 groups |
| Maximum aperture | f/3.3 – 4.0 |
| Minimum focus distance | Wide-angle: 4 inches (0.1m) to infinity, Telephoto: 20 inches (0.5m) to infinity (from front of camera) Super Macro: 2 inches (0.05m) (Focal length fixed at: 12mm) |
| Maximum magnification | 0.21x (equivalent to 1.3x in 35mm format) |
| Area covered at maximum magnification | 1.1 x 0.9 inches (27.3mm x 20.3mm) |
| Monitor LCD | 2.5-inch (6.4cm) digital-interface micro-reflection TFT color monitor Total pixels: Approximately 115,000 |
| Shutter | CCD electronic shutter and mechanical shutter |
| Shutter speed range | 4 - 1/1000 seconds |
| Autofocus system | Video AF |
| Autofocus areas | Wide (five-point AF) or Spot selectable |
| Metering | Multi-segment (256 segments) / Spot selectable |
| Exposure control | Programmed AE |
| Automatic Digital Subject Program Selection | Portrait, Sports action, Landscape, or Sunset is automatically selected (Manual selection is also possible) Night portrait/Night view, Super Macro, Text is set manually only. |
| Exposure compensation | ±2EV in 1/3 increments |
| Flash range | Wide-angle: Approximately 0.7 – 7.9 ft. (0.2 – 2.4m) Telephoto: Approximately 1.6 – 6.6 ft. (0.5 – 2.0m) (from front of camera, camera sensitivity: AUTO) |
| Flash modes | Autoflash, Autoflash with red-eye reduction, Fill-flash, Flash cancel |
| Continuous advance | Approximately 1.6 frames per second* up to 4 frames * Actual speed may vary depending upon the subject and camera settings. |
| Self-timer | Approximately 10 seconds |
| Multi frame | To capture 9 sequential images in a 3x3 grid in a single frame |
| Image pasting | Embeds an image within another image. |

| Movie recording | Recording time dependent on memory card capacity. Frame rate: 15 frames per second, 30 frames per second Night Movie, Movie frame capture, Movie clip capture |
| --- | --- |
| Audio | Audio recording: 180 minutes (maximum)* *128MB MB memory card is required. Audio caption: 15 seconds (maximum) Voice memo: 15 seconds (maximum) Monaural audio only |
| White-balance control | Automatic, Preset (Daylight, Cloudy, Tungsten, Fluorescent) |
| Color modes | Color, Black and White, and Sepia |
| Noise reduction | Automatic |
| Digital zoom | Maximum 4x. Digital zoom can be disabled. |
| E-mail Copy function | Creates a compressed 640 x 480 JPEG image for data transfer |
| Crop frame | Trims parts of captured still pictures and save the image as a separate file. |
| Date imprinting | Year/month/day (Format can be changed.) Month/day/hour:minute (Format can be changed.) Imprinting can be disabled. |
| Image quality modes | Economy, Standard, Fine |
| Number of recorded pixels (Still images) | 2560 x 1920, 2048 x 1536, 1600 x 1200, 640 x 480 |
| Number of recorded pixels (Movie clips) | 320 x 240 |
| Storage capacity | Approximate capacity with 15MB internal memory: 2560x1920 2048x1536 1600x1200 640x480 Fine* 6 frames 9 frames 14 frames 71 frames Standard* 11 frames 17 frames 28 frames 103 frames Economy* 22 frames 33 frames 48 frames 155 frames Movie (320x240) 15 frames per second: 41 seconds 30 frames per second: 21 seconds Audio recording 31 minutes 43 seconds *Still images recorded without voice memo or audio caption **Actual number of images may vary depending upon the subject and memory card. |
| File formats | JPEG, Motion JPEG (MOV), WAVE DCF 2.0-compliant DPOF-compliant (Supported by printing functions in version 1.1) Exif 2.2 |
| Folder name formats | Standard, Date |
| Printing output control | Exif Print, PRINT Image Matching II, PictBridge |
| Menu languages | English, German, French, Spanish, Italian, Swedish, Russian, Chinese (Simplified and Complicated), Japanese, and Korean |
| Recording media | Secure Digital (SD) Memory Cards, MultiMedia Cards, 15MB internal storage |
| Computer interface | USB: Full-speed 12 Mbps data transfer with a USB 2.0 compatible computer. |
| Remote camera | Live images without audio viewed with a computer |
| Battery | One NP-700 Lithium-ion Battery |
| Battery performance (Recording) | Approximate number of recorded images: 150 frames. Based on CIPA (Camera & Imaging Products Association) measurements, when using standard battery (Lithium-ion battery) and a SD memory card |
| External power source | 4.7V DC with specified AC adapter (sold separately) |

| Dimensions (W x H x D) | 3.3 x 2.2 x 0.9 inches (83.5 x 56 x 22 mm) |
| --- | --- |
| Weight | Approximately 4.1 ounces (115g) (without battery and recording media) |
| Operating temperature | 32-104°F (0-40ºC) |
| Standard accessories | Lithium-ion Battery NP-700, Battery Charger BC-800, Hand Strap HS DG130, USB, Cable USB-3, Digital Camera Software CD-ROM, AV Cable AVC-500 |
| Optional accessories | AC Adapter set AC-4 or AC-5, Metal Chain Neck Strap NS-DG100, Marine Case MC-DG500 *Availability varies with region. |

Konica Minolta Marine Case for the

DiMAGE X60 Digital Camera

Specifications

| Maximum depth (underwater) | 131 ft. (40m) |
| --- | --- |
| Weight | 8.5 oz. (240g) (Case only) |
| Dimensions (WxHxD) | 4.8 x 3.3 x 2.1 inches (122.5 x 83.5 x 52.5 mm) excluding protrusions |
| Standard accessories | Hand strap, O-ring grease, Desiccant |
| Optional accessories | O-ring set OR-GS400 |

System Requirements

Compatible computers when the camera is used as mass storage device:

IBM PC/AT compatible computers with Windows XP (Home/Professional), Windows Me, Windows 2000 Professional, Windows 98*, or Windows 98 Second Edition* and with a USB port as standard interface.

Apple Macintosh computers with preinstalled Mac OS 9.0 – 9.2.2, Mac OS X v10.1.3-10.1.5, v10.2.1-10.2.8, v10.3-10.3.8 and with a USB port as standard interface.

*	Users with Windows 98 and Windows 98 Second Edition operating systems must install dedicated driver software included in the DiMAGE X50 package.

Minimum system requirements for the remote camera function:

| Computers | IBM PC/AT compatible computers with a USB port as standard interface |
| --- | --- |
| CPU | Pentium II 300MHz or later processor (*1) |
| Operating systems | Windows XP (Home/Professional), Me, 2000 Professional, or 98 Second Edition |
| RAM | 128 MB of RAM. 256 MB with Windows XP. (*1) |
| Hard-disk space | Approx. 200 MB of free hard-disk space |
| Monitor | 800 x 600 monitor capable of displaying 16-bit color quality. |
| Tested applications | Microsoft NetMeeting, Windows Messenger (*2) |
| Other | CD-ROM drive |

*1	The CPU and RAM must satisfy the requirements of the operating system.

*2 	The application software must be guaranteed by the manufacturer to work with the operating system.

•	The computer and operating system must be guaranteed by their manufacturers to support USB interface.

•	Problems may be encountered depending on what other USB devices are being used in parallel with this product.

•	Only a built-in USB port is supported. Problems may be encountered when the camera is connected to a USB hub.

•	Normal operation may not be possible even when all the system requirements are met.

Specifications, accessories and system requirements are subject to change without notice.

DiMAGE, CxProcess are trademarks or registered trademarks of Konica Minolta Photo Imaging, Inc.

Windows is either a registered trademark or a trademark of Microsoft Corporation in the United States and/or other countries. Macintosh is a trademark or registered trademark of Apple Computer Inc. Other corporate names and product names are trademarks or registered trademarks of their respective companies.

###