# Konica Minolta Maxxum 50

35mm Single-Lens Reflex Camera

## Technical Specifications

| Camera type | 35mm autofocus SLR with autoexposure (AE) and a built-in flash |
| --- | --- |
| Lens mount | Minolta A mount |
| Autofocus system | Detection system: TTL phase-detection Autofocus sensors: CCD line sensors (3-point AF system with a center cross-hair sensor) Autofocus sensitivity range: EV -1 – 18 (ISO 100) AF illuminator: Built-in flash; Automatically activates in low light, low-contrast situations. Range: Approximately 3.3 – 16.4 ft. (1 - 5m) Autofocus areas: Wide focus area; Spot focus area Predictive focus control: Multi-dimensional predictive focus control for moving subjects Focus modes: Autofocus, Manual focus AF modes: Automatic AF, Single-shot AF, Continuous AF |
| Exposure system | Metering: TTL, 2-segment metering Metering cell: 2-segment SPC (silicon photocell) Metering range: EV 4-20 (ISO 100, f/1.4 lens) Exposure control: Programmed AE, Aperture priority, Shutter priority, Manual Subject programs: Portrait, Landscape, Close-up, Sports action, Night portrait Shutter and aperture control: In 0.5 EV increments Exposure compensation: +/- 3 EV in 0.5 EV increments Exposure bracketing: 3 exposures in 0.5 or 1 EV increments ISO settings: Automatic with DX-coded film between ISO 25 – 3200 in 1 EV increments. (Non-DX-coded film: ISO is set to 25.) ISO 25 - 1000 with flash AE lock: Exposure is locked with focus. |
| Shutter | Type: Electronically-controlled, vertical-traverse, focal-plane shutter Speed range: 30 - 1/2000 second, Bulb (up to approximately TBA hours With fresh batteries) Flash-sync speed: 1/90 second or slower |
| Flash | Flash metering: Pre-flash TTL, ADI* *ADI flash metering with D lens and the built-in flash, Program Flash 5600HS(D), 3600HS(D) or 2500(D). Type: Built-in Guide number: 39 feet (12m) at ISO 100) Usable flash range: 3.3 – 13.1 ft. (1 - 4m) Flash coverage: 28mm angle of view Flash modes: Autoflash, Autoflash with red-eye reduction, Fill flash, Fill flash with red-eye reduction, Flash cancel Recycling time: Approximately 5 seconds |
| Viewfinder | Type: Eye-level fixed roof mirror Focusing screen: Spherical acute matte Field of view: 90% (vertical) x 90% (horizontal) Magnification: 0.75x (with 50mm lens focused at infinity) Eye relief: 17.2mm (11.3mm from the eyepiece frame) Diopter: -1 diopter Eyepiece cup: Fixed |
| Film transport | Film advance: Single-frame advance, Continuous advance Continuous advance speed: Maximum 1.7 frames per second Loading: Automatic loading Rewinding: Automatic rewind, Manual rewind Rewind time: Approximately 8 seconds with 24-exposure film |
| Self-timer | 10 seconds |
| IR remote control receiver | Date model only IR Remote Control RC-3 (sold separately) |
| Power | Two 3V CR2 lithium batteries |
| Battery performance | Approximate battery performance with CR2 lithium batteries: Condition A Flash use 68 ºF (+20 ºC) 14 ºF (-10 ºC) 0 % 30 rolls 24 rolls 50 % 14 rolls 11 rolls 100 % 9 rolls 7 rolls Condition B Flash use 68 ºF (+20 ºC) 14 ºF (-10 ºC) 0 % 45 rolls 35 rolls 50 % 18 rolls 14 rolls 100 % 11 rolls 9 rolls Condition A: 28-100mm f/3.5-5.6(D) focused from infinity to 6.6 ft. (2m) three times, and the shutter-release button held partway down for ten seconds before each exposure. Other basic photographic procedures are performed. Condition B: 28-100mm f/3.5-5.6(D) focused from infinity to 6.6 ft. (2m), and the shutter-release button held partway down for five seconds before each exposure. Other basic photographic procedures are performed. • With 24-exposure film, fresh battery, standard AF zoom lens (except for xi or Power Zooms). Exposures taken at a rate of 2 rolls per month. • Battery performance will vary with usage conditions |
| Dimensions (WxHxD) | 5.31 x 3.62 x 2.62 inches (135 x 92 x 66.5 mm) |
| Weight | 11.8oz. (335g) without batteries |

Specifications are subject to change without notice.

#   #   #