### Konica Minolta Maxxum 70

### 35mm Single-Lens Reflex Camera

### Technical Specifications

| Camera type | 35mm autofocus SLR with autoexposure (AE) and a built-in flash |
| --- | --- |
| Lens mount | Minolta A mount |
| Autofocus system | Detection system: TTL phase-detection Autofocus sensors: CCD line sensors (9-point AF system with a center cross-hair sensor) Autofocus sensitivity range: EV -1 – 18 (ISO 100) AF illuminator: Built-in flash. Automatically activates in low light, low-contrast situations. Range: Approximately 3.3 – 16.4 ft. (1 - 5m) Autofocus areas: Wide focus area. Any local focus area can be selected from the 9-point sensors. Predictive focus control: Multi-dimensional predictive focus control for moving subjects Focus modes: Autofocus, Manual focus AF modes: Automatic AF, Single-shot AF, Continuous AF, DMF |
| Exposure system | Metering: TTL, 14-segment honeycomb-pattern metering Metering cell: 14-segment honeycomb-pattern SPC (silicon photocell) Metering range: 14-segment honeycomb-pattern : EV 1-20 Spot: EV 4-20 (ISO 100, f/1.4 lens) Exposure control: Programmed AE (with PA/Ps Creative Program Control), Aperture priority, Shutter priority, Manual Subject programs: Portrait, Landscape, Close-up, Sports action, Night portrait Shutter and aperture control: In 0.5 EV increments Exposure compensation: +/- 3 EV in 0.5 EV increments Exposure bracketing: 3 exposures in 0.3, 0.5, 0.7 or 1 EV increments ISO settings: Automatic with DX-coded film between ISO 25 - 5000 in 1/3 EV increments. (With non-DX-coded film the ISO of the previous roll is set.) Manual with DX-coded film between ISO 6 - 6400 in 1/3 EV increments. ISO 25 - 1000 with flash AE lock: Exposure is locked with focus. Exposure is locked with the AE-lock button |
| Shutter | Type: Electronically-controlled, vertical-traverse, focal-plane shutter Speed range: 30 - 1/2000 seconds, Bulb (up to approximately TBA hours with fresh batteries) Flash-sync speed: 1/90 second or slower. With shutter speeds faster than 1/90 second, camera automatically switches to high- speed sync(HSS)*. (*available with Program Flash 5400HS, 5600HS(D), and 3600HS(D).) Wireless/Remote flash-sync speed: 1/45 second or slower. |
| Flash | Flash metering: Direct TTL OTF (ADI or TTL can be selected with a custom function.) Type: Built-in Guide number: 52 feet (16m) at ISO 100 Flash coverage: 28mm angle of view Flash modes: - In programmed AE and subject program selection modes: Autoflash, Fill flash, Flash cancel, Red-eye reduction (using pre- flash), Wireless/Remote off-camera flash (with Program Flash 5600HS(D) and 3600HS(D)), High-speed sync(HSS)* *available with Program Flash 5400HS, 5600HS(D), and 3600HS(D) Recycling time: Approximately 4 seconds |
| Viewfinder | Type: Eye-level fixed roof mirror Focusing screen: Spherical acute matte Field of view: 90% (vertical) x 90 % (horizontal) Magnification: 0.7x (with 50mm lens focused at infinity) Eye relief: 16mm (13mm from the eyepiece frame) Diopter: -2 to +1 Diopter adjustment: Yes Eyepiece cup: Removable |
| Film transport | Film advance: Single-frame advance, Continuous advance Continuous advance speed: Maximum 3 frames per second Loading: Automatic loading Rewinding: Automatic rewind, Manual rewind Rewind time: Approximately 8 seconds with 24-exposure film |
| Self-timer | 10 seconds |
| IR remote control receiver | IR Remote Control RC-3 (sold separately) *IR remote control capable model only |
| Audio signal | Audio signal can be disabled. Other functions: 15 custom functions) Multiple-exposure mode |
| Power | Two 3V CR2 lithium batteries Battery-condition indication: 3-stage indicator appears when the camera is turned on. |

| Battery performance | Approximate battery performance with CR2 lithium batteries: Condition A Flash use 68 ºF (+20 ºC) 14 ºF (-10 ºC) 0 % 30 rolls 24 rolls 50 % 14 rolls 11 rolls 100 % 9 rolls 7 rolls Condition B Flash use 68 ºF (+20 ºC) 14 ºF (-10 ºC) 0 % 45 rolls 35 rolls 50 % 18 rolls 14 rolls 100 % 11 rolls 9 rolls Condition A: 28-100mm f/3.5-5.6(D) focused from infinity to 6.6ft.(2m) three times, and the shutter-release button held partway down for ten seconds before each exposure. Other basic photographic procedures are performed. Condition B: 28-100mm f/3.5-5.6(D) focused from infinity to 6.6ft.(2m), and the shutter-release button held partway down for five seconds before each exposure. Other basic photographic procedures are performed. • With 24-exposure film, fresh battery, standard AF zoom lens (except for xi or Power Zooms). Exposures taken at a rate of 2 rolls per month. • Battery performance will vary with usage conditions |
| --- | --- |
| Dimensions (WxHxD) | 5.31 x 3.62 x 2.62 inches (135 x 92 x 66.5(D) mm) |
| Weight | 13.2oz. (375g) without batteries, accessories or attachments |

Specifications are subject to change without notice.

#   #   #