Konica Minolta Zoom 60 Date

35mm Point-and-Shoot Camera

Specifications

| Camera type | 35mm lens-shutter camera |
| --- | --- |
| Lens | Focal length: 35 - 60mm Lens construction: 4 elements in 4 groups (includes two aspheric elements) Maximum aperture: f/6.3 – f/10.3 Minimum focus distance: Wide: 3 ft. (0.9m) Telephoto: 3.9 ft. (1.2m) |
| Viewfinder | Type: Van Albada zoom Field of view: 80% at 9.8 ft. (3m) Magnification: 0.36 – 0.57x Diopter: -1 at infinity |
| Autofocus | Active AF system |
| Autoexposure | Metering: Center-weighted Control: Programmed AE Metering range (ISO 100): Wide: EV 7 – 15 Telephoto: EV 8 – 16 Shutter speeds: 1/3 - 1/250 second ISO setting: DX-coded-film is automatically set to ISO 100 or 400. Non-DX-coded film is set to ISO 100. |
| Film transport | Automatic loading, Automatic rewind, Manual rewind |
| Flash | Control: Electronic flashmatic Range: With ISO 100 film: Wide: 3 – 7.2 ft. (0.9 – 2.2m) Telephoto: 3.9 – 4.6 ft. (1.2 – 1.4m) With ISO 400 film: Wide: 3 – 13.8 ft. (0.9 – 4.2m) Telephoto: 3.9 – 8.2 ft. (1.2 – 2.5m) * with color negative film Recycling time: Maximum 8 seconds Red-eye reduction: With red-eye reduction lamp (LED) Flash/Shooting modes: Autoflash (in low-light), Autoflash with red-eye reduction, Flash cancel, Fill-flash, Self-timer |
| Self-timer | 10 seconds |
| Date imprinting | Year/month/day (Format can be changed.) Day/hour/minute Imprinting can be disabled. |
| Power | Battery: Two AA alkaline or carbon-zinc batteries (Use of alkaline batteries is recommended.) Battery performance: Approximately twelve 24-exposure rolls Based on Minolta's standard test method: flash used with 50% of the exposures with fresh alkaline batteries. |
| Dimensions (WxHxD) | 4.5 x 2.6 x 1.7 in. (115 x 67 x 44mm) |
| Weight | 6.7 oz. (190 g) without batteries |

Specifications are subject to change without notice.

#   #   #