Konica Minolta Zoom 80c Date

Compact 35mm Point-and-Shoot Camera

Specifications

| Camera type | 35mm lens-shutter camera |
| --- | --- |
| Lens | Focal length: 35 - 80mm Lens construction: 5 elements in 5 groups (includes one aspheric element) Maximum aperture: f/6 – f/12 Minimum focus distance: 3 ft. (0.9m) |
| Viewfinder | Type: Real-image zoom viewfinder Field of view: 80% or larger at 9.8 ft. (3m) Magnification: TBD Diopter: -1 at 9.8 ft. (3m) |
| Autofocus | Active AF system |
| Autoexposure | Metering: Average Control: Programmed AE Metering range (ISO 100): Wide: EV 7 - 16 Telephoto: EV 7 – 16 Shutter speeds: 1/2 - 1/500 seconds ISO setting: DX-coded-film is automatically set to ISO 100 or 400. Non-DX-coded film is set to ISO 100 |
| Film transport | Automatic loading, Automatic rewind, Manual rewind |
| Flash | Control: Electronic flashmatic Range: With ISO 100 film: Wide: 3.3 – 9.9 ft. (1 – 3m) Telephoto: 3.3 – 4.5 ft. (1 – 1.4m) With ISO 400 film: Wide: 3.3 – 19.7 ft. (1 – 6m) Telephoto: 3.3 – 9.2 ft. (1 – 2.8m) * with color negative film Recycling time: 7 seconds (approximately) Red-eye reduction: With red-eye reduction lamp Flash/Shooting modes: Autoflash (in low-light), Self-timer/remote control, Fill-flash, Flash cancel, Landscape/night view, Slow shutter sync |
| Self-timer | 10 seconds |
| Date imprinting | Year/month/day (Format can be changed.) Day/hour/minute Imprinting can be disabled. |
| Power | Battery: One CR2 Battery performance: Twelve 24-exposure rolls (approximately) Based on Minolta's standard test method: flash used with 50% of the exposures with fresh batteries |
| Dimensions (WxHxD) | 4.4 x 2.5 x 1.7 inches (110.5 x 63 x 42.5 mm) |
| Weight | 6.3 ounces (180 g) without battery |

Specifications are subject to change without notice.