Konica Minolta R1 SUPER 1400 Digital Minilab System

Specifications

| Product Name | R1 SUPER 1400 |
| --- | --- |
| System configuration | Input section(workstation) and output section(printer processor) separated units |
| Imaging section | Independent B/G/R line photometry using 3-line CCD; film shift method |
| Input media | film | Color negative film: 135, APS, 110, 120 (6×4.5; 6×9) Color reversal film: 135,APS,120 (6×4.5; 6×9); Slide mount (135, APS) B&W, Sepia film: 135 |
|  | Digital media | FD, SM, MS, CF, SD MMC, Micro Drive, CD-R; Prints (for P-to-P service) |
| Printing capacity 135 Negative film (24exp.) | 3R; 127×89mm | 1,400 prints/hour |
|  | 4R; 152×102mm | 1,200 prints/hour |
| Printing capacity Digital camera 3 million pixels | 3R; 127×89mm | 1,400 prints/hour |
|  | 4R; 152×102mm | 1,200 prints/hour |
|  | 8R; 203×254mm | 450 prints/hour |
| Exposure system | Beam Convergence Head (BCH) |
| Paper width | 89, 102, 120, 127, 152, 165, 178, 203, 210, 216 mm |
| Processing time dry-to-dry | 2 minutes, 25 seconds |
| Dimensions | Input section | 850 (W) × 1,303 (H) × 900 (D) mm |
|  | Output section | 1,903 (W) × 915 (H) × 985 (D) mm |
| Weight | Input section | Approximately 100kg including dedicated desk |
|  | Output section | Approximately 415kg |
| Foot print | Input section | 1.50 | 0.70 |
|  | Output section |  | 1.50 |
| Monitor | 17-inch CRT display |
| Magazine | Single magazine |
|  | Double magazine optional |

Specifications and design of products may be improved or otherwise modified without prior notice.

#   #   #