Konica Minolta DG-5W 4 Megapixel

Waterproof Digital Camera

Specifications

| Number of effective pixels | Approximately 4.0 million |
| --- | --- |
| CCD | 1/2.5" interline primary-color CCD, total pixels: 4.2 million |
| Lens construction | 14 elements in 12 groups |
| Focal length | 4.6-12.8mm (35mm equivalent: 28-78mm) |
| Maximum aperture | f/2.8-f/4.5 |
| Storage media | SD memory card or MMC |
| File formats | JPEG, DCF 2.0 compliant, DPOF compliant (Supported by printing functions in version 1.1), Exif 2.2, Motion JPEG (AVI) with monaural audio |
| PictBridge | Supported |
| Number of recorded pixels (still) | 2272x1704 Fine or Standard, 1600x1200 Standard, 1280x960 Standard, 640x438 Standard |
| Storage capacity | Approximate storage capacity of a 16MB SD memory card: 2272x1704: Fine 8, Standard 16 1600x1200: Standard 33 1280x960: Standard 24 640x480: Standard 133 |
| LCD monitor | 2.0" low-temperature polysilicon TTF color LCD, approximately 210,000 pixels Field of view: approximately 100% Reflective and transparent hybrid |
| What you see on LCD | Recording mode: Live view and camera status Play mode: Playback images (single frame or six-frame index, magnified images up to 6x, scrollable, movie) |
| Autofocus system | Video AF system |
| Focus area | Center |
| Focus mode | Single-shot AF |
| Focus lock | Available by pressing shutter-release button halfway down |
| Exposure mode | Programmed AE |
| Metering system | 256-cell multi cell metering |
| Exposure compensation | +/- 2EV in 1/3EV increments |
| Shutter system | CCD electronic shutter and electronically-controlled mechanical shutter |
| Shutter speed | 4 - 1/1000 second |
| Flash modes | Auto, Fill-in, No Flash |
| Flash range | Wide angle: up to approximately 40 feet, Telephoto: up to approximately 20 feet |
| White balance | Auto, Preset (Daylight, Cloudy, Fluorescent, Tungsten), Custom |
| Color modes | Color, Black & White, Sepia |
| Self-timer | 10 seconds and 2 seconds |
| Noise reduction | Available |
| Date imprint | Available |
| Movie file format | Motion JPEG (AVI) with monaural audio |
| Number of recorded pixels (movie) | 320x240 |
| Movie frame rate | Maximum 15 frames per second |
| Movie recording time | Maximum 5 minutes on SD, Maximum 30 seconds on MMC |
| Audio functions | After-recording & Voice Memo |
| Maximum recording (audio) | 30 seconds |
| Camera start-up time | Approximately 1.0 second (between Power ON and LCD ON) |
| Battery | Rechargeable Lithium-ion Battery |
| External power supply | DC 6V with specified optional AC Adapter |
| Battery performance | Approximately 240 frames based on CIPA test standards |
| PC interface | USB Full-speed 12Mbps data transfer with USB 2.0 compatible computer |
| AV output | NTSC, PAL (selected on camera) |
| Dimensions (WxHxD) | 4.9 x 2.7 x1.8 inches |
| Weight | Approximately 13.8 oz (not including battery, media or strap) |
| Waterproofness | JIS Class 7, not for underwater photography |
| Dustproofness | JIS Class 6 |
| Bundled accessories | Rechargeable Lithium-ion Battery NP-800, Charger BC-900, Neck strap, AV Cable, USB Cable, 16MB SD memory card, DiMAGE Viewer CD-ROM |
| Optional accessories | AC Adapter AC-DG5W, Camera Case (TBD) |
| Supported OS | Windows XP (Home & Professional), Windows Me, Windows 2000 Professional and Windows 98 SE, Mac OS 9.0-9.2.2, Mac OSX v10.1.3-10.1.5, 10.2.1-10.2.8, 10.3-10.3.7 |

Specifications are subject to change.

#   #   #