Konica Minolta DiMAGE Scan Elite 5400 II

Film Scanner

Specifications

| Type | 35mm film scanner |
| --- | --- |
| Film type | 35mm film (color/black & white, negative/positive) |
| Optical resolution | 5400 dpi |
| Scan sizes | 25.06 x 37.25mm 35mm Film Holder scan area: 24 x 36mm Maximum input pixels: 5328x7920 pixels |
| Scanning method | Moving film, fixed sensor, single-pass scan |
| Image sensor | 3-line color CCD with 5340 pixels per line |
| Filter | Primary color filter |
| Multi-sample scanning | 16x, 8x, 4x, 2x, Off |
| Continuous scan | 35mm film holder: Maximum 6 frames Slide mount holder: Maximum 4 frames |
| A/D conversion | 16 bit per color channel |
| Output data | 8 bit and 16 bit per color channel |
| Dynamic range | 4.8 (computed value) |

| Scan time | Windows Macintosh Index scan 12 seconds 16 seconds Prescan 8 seconds 9 seconds Scan 25 seconds 30 seconds * Index scan with the six-frame 35mm slide holder. * With positive film. * Approximate time with maximum optical resolution(5400dpi), 8-bit color depth, No auto focus, No multi-sample scanning, No cropping, No image corrections, No auto exposure, No color matching, No Digital ICE4 or Pixel Polish processing. * Scan time varies with the system environment, film images, scanner preferences and functions used. * Scan time is longer for negative film than positive film. * Scan time is longer when Digital ICE4 or color matching function is on. Scan time Test Conditions: Windows: CPU: Pentium 4 3.2 GHz, OS: Windows XP Professional RAM: 1GB HDD free space: 69GB Interface: USB 2.0 port built-in Application: Adobe Photoshop 7.0.1, 80% of memory allocated to application. Macintosh: CPU: PowerPC G5 Dual 2GHz OS: Mac OS X v10.3.6 RAM: 1.5GB HDD free space: 61GB Interface: USB 2.0 port built-in Application: Adobe Photoshop 7.0.1, 80% of memory allocated to application. |
| --- | --- |
| Interface | USB 2.0 (1.1 compatible) |
| Focusing | Autofocus and manual focus (motor drive / manual), Center / Spot focus area |
| Light source | White LED |
| Power requirements | 100-120 V AC, 50/60 Hz for North America with the supplied AC adapter. |
| Power consumption | Maximum 20W ENERGY STAR compliant |
| Dimensions (WxHxD) | 72.8 x 6.5 x 13.6 in. (70 x 165 x 345mm) |
| Weight | Approximately 3.3 lb. (1.5 kg) |
| Standard accessories | 35mm Film Holder FH-M20, Slide Mount Holder SH-M20, USB Cable UC-2 (USB2.0 compatible), AC Adapter AC-U26, CD-ROM For DiMAGE Scan Elite 5400 II, Adobe Photoshop Elements 2.0, Reset tool RT-M10 |

System Requirements

|  | IBM PC/AT compatible computers(*1) | Macintosh(*1) |
| --- | --- | --- |
| Interface | USB 2.0 / 1.1 | USB 2.0 / 1.1 |
| CPU (*2) | Pentium166MHz or later processor | PowerPC G3 or later |
| Operating systems | Windows 98 Windows 98 Second Edition Windows Me Windows 2000 Professional Windows XP Professional Windows XP Home Edition | Mac OS 9.2.2 Mac OS X v10.1.3 to 10.1.5, v10.2.1 to 10.2.8, v10.3 to 10.3.6 |
| RAM (*2) | 128 MB or more of RAM | 128 MB or more of RAM (free memory space excluding memory used for applications and OS) |
| Hard-disk space | 600 MB or more on the startup disk. | 600 MB or more on the startup disk. |
| Monitor | 800x600 monitor capable of displaying High Color (16-bit) is required. 1024x768 monitor is recommended. | 800x600 monitor capable of displaying at least 32,000 colors is required. 1024x768 monitor is recommended. |
| Tested applications (*3) | Adobe Photoshop 6.0.1, 7.0.1, CS(8.0.1), Adobe Photoshop Elements 2.0, Paint Shop Pro 8, and Corel PHOTO-PAINT 11. | Adobe Photoshop 6.0.1, 7.0.1, CS (8.0.1), Adobe Photoshop Elements 2.0 |
| Recommended interface (*3) | Adaptec, Inc.: USB2 Connect 3100, USB2 Connect 5100, Duo Connect Belkin: Hi-speed USB 2.0 5-Port PCI Card, USB 2.0 Hi-Speed 3-Port Low Profile PCI Card Preinstalled USB port. | Belkin: Hi-speed USB 2.0 5-Port PCI Card, USB 2.0 Hi-Speed 3-Port Low Profile PCI Card Preinstalled USB port. |

(*1) Not compatible with Fast User Switching (Windows XP and Mac OS X v.10.3).

(*2) Necessary to meet the requirements recommended for use with the OS.

(*3) Operation must be guaranteed by the manufacturers to work with the OS. For details, contact the respective manufacturer.

16-bit output with Digital ICE4

Windows:

CPU: Pentium 166MHz or later, Pentium III or later recommended. / RAM: 256MB or more, 512MB or more recommended. / Hard Disk Space (Start up disk): 3GB or more, 6GB or more recommended.

Macintosh:

CPU: PowerPC G3 or higher, PowerPC G4 or higher recommended. / RAM: At least 320 MB of RAM. (512 MB or more recommended) / Hard Disk Space (Start up disk): 3GB or more, 6GB or more recommended.

Pixel Polish

Windows:

CPU: Pentium 166MHz or later, Pentium III or later recommended. / RAM: 256MB or more, 512MB or more recommended. / Hard Disk Space (Start up disk): 1.2GB or more, 2GB or more recommended.

Macintosh:

CPU: PowerPC G3 or higher, PowerPC G4 or higher recommended. / RAM: At least 256 MB of RAM. (512 MB or more recommended) / Hard Disk Space (Start up disk): 1.2GB or more, 2GB or more recommended.

Specification figures are based on Konica Minolta's standard test method. Error-free operation is not

guaranteed for any of the systems recommended.

# Specifications, accessories and system requirements are subject to change without notice.

# * Konica Minolta is a trademark of Konica Minolta Holdings, Inc. DiMAGE, DiMAGE Scan and

# Pixel Polish are trademarks or registered trademarks of Konica Minolta Photo Imaging, Inc.

# * Windows and Windows XP are trademarks or registered trademarks of Microsoft Corporation in the

# United States and/or other countries.

# * Apple, Macintosh and Mac OS are trademarks or registered trademarks of Apple Computer, Inc. in the

# United States and/or other countries.

# * Digital ICE4, Digital ICE, Digital ROC, Digital GEM and Digital SHO are trademarks of Eastman

# Kodak Company.

# * Other corporate and product names are trademarks or registered trademarks of their respective companies.

#   #   #