# Minolta DiMAGE E201 Digital Camera

### Specifications

| CCD | 1/1.75-type interline primary-color CCD with a total of 2.3 million pixels |
| --- | --- |
| Number of effective pixels | 2.15 million |
| A/D conversion | 12 bits |
| Sensitivity | Normal: ISO 85 equivalent High: ISO 340 equivalent |
| Aspect ratio | 3:2 |
| Focal length | 8.2mm (35mm equivalent: 38mm) |
| Lens construction | 5 elements in 4 groups (includes 3 elements with 4 aspheric surfaces) |
| Maximum aperture | f/3.0 |
| Minimum Focus Distance | Approximately 2 ft. (0.6m) |
| Macro focus range | Approximately 1 ft. – 2 ft. (0.3 – 0.6 m) from the front of the lens |
| Viewfinder | Reversed Galilean viewfinder |
| Liquid Crystal Display (LCD) | 46mm (1.8 inch) color monitor Total number of pixels: 77,000 |
| Field of view | Approximately 90% |
| Shutter | CCD electronic shutter and mechanical shutter |
| Shutter speed | 1/500 - 2 seconds |
| Autofocus | Video AF system |
| Focus lock | Available with pressing the shutter button part-way down |
| Metering | Center-weighted |
| Exposure modes | Programmed AE |
| Exposure compensation | +/– 2 EV in 1/2 increments |
| AE lock | Available with pressing the shutter button part-way down |
| Flash range | Approximately 2 ft. – 2.5 ft. (0.6 – 2.5 m) at ISO 85 equivalent Approximately 2 ft. – 16.4 ft. (0.6 – 5 m) at ISO 340 equivalent |
| Flash mode | Autoflash, Fill-flash, Flash cancel, Autoflash with red-eye reduction, Fill-flash with red-eye reduction, Macro (flash is cancelled) |
| Flash recycling time | Approximately 10 seconds |
| Continuous drive advance | Approximately 1 fps |
| Self-timer | Approximately 10-second delayed release |
| Remote control | IR Remote Control RC-3 (sold separately) |
| Movie recording | Movie clips with audio (maximum 60 seconds) |
| Color modes | Color, black and white |
| White balance | Automatic, Manual (Preset - Daylight, Fluorescent, Tungsten) |
| Sharpness settings | Three levels (Soft, Normal, Hard) |
| Digital zoom | 2x, 1.4x |
| Delete function | Available (single frame or all frames ) |
| Format function | Available in the setup mode |
| Image compression mode | Economy, Standard, Fine, Super fine |
| Number of pixels | Still images: 1792 x 1200 (full size), 800 x 600 (half size) |
| Storage capacity (8 MB) (Full File Size) | Super fine: 1 frame; Fine: 9 frames; Standard: 24 frames; Economy: 47 frames; Movie:40 seconds |
| File format | Exif 2.1 (JPEG, TIFF), Motion JPEG (AVI), DCF1.0-compliant, DPOF compliant (Supported by printing functions in version 1.1) |
| Exif tag information | Date and time, Shutter speed, Aperture value, Exposure compensation value, Flash on/off, Camera sensitivity, etc. |
| Recording medium | CompactFlash card Type I |
| PC interface | USB version 1.1 |
| Video output | NTSC, PAL (can be selected by user) |
| Audio signals | Tone indicates operation. Audio signal can be disabled. |
| Power | Four AA Alkaline or four AA Ni-MH batteries |
| Battery performance | Playback: 120 min. (approximately) with alkaline batteries Recording: 120 frames (approximately) (Based on Minolta’s standard test method: alkaline batteries, LCD monitor on, flash used 50% of the frames, standard image quality, full-size images.) |
| External power source | 6V DC with specified AC adapter (sold separately) |
| Dimensions (WxHxD) | 4.46 x 2.5 x 2.3 inches (114 x 65 x 45 mm) |
| Weight | Approximately 7 ounces (210g) (without batteries and CompactFlash card) |
| System Requirements | IBM PC/AT compatible computer with preinstalled Windows ME, Windows 2000, Windows 98 or Windows 98 SE and a built-in USB port Power Macintosh G4 series, G3 series, iMac series, iBook or PowerBook G3 with preinstalled Mac OS 9.0 – 9.1 and a built-in USB port |
| Accessories | Standard: Hand Strap for DiMAGE E201 & Dimâge 2300 HS-DG201 Camera Case for DiMAGE E201 & Dimâge 2300 CS-DG201 USB Cable for DiMAGE E201 & Dimâge 2300 USB-300 Video Cable for DiMAGE E201 & Dimâge 2300 VC-200 CF Card (8 MB), AA Alkaline Batteries, CD-ROM for DiMAGE E201 CD-ROM for PhotoDeluxe Home Edition 4.0 Windows, CD-ROM for PhotoDeluxe 2.0 Macintosh Optional: IR Remote Control RC-3; AC Adapter AC-1L |

Specifications, accessories and system requirements are subject to change without notice.

#   #   #