Minolta Program/Maxxum Flash 2500 (D)

Specifications

| Type | Auto-electronic flash |
| --- | --- |
| Compatible cameras* | Minolta Maxxum 9, 9Ti, 7, 5, 4, 3, and si-, xi-, and i-series AF SLRs. DiMAGE 5, DiMAGE 7 series digital cameras, DiMAGE A1, and the DiMAGE Z1. |
| Flash mount | Minolta dedicated shoe mount with automatic lock |
| Guide number | 82 (in feet at ISO 100) / 25 (in meters at ISO 100) |
| Flash coverage | 28mm angle of view |
| Bounce flash | Flash head can be tilted between 0 - 90˚ (click-stop at 60˚). |
| AF illuminator* | Automatically activates in low light and low-contrast situations. Range: Approximately 3.3 – 16.4 ft. (1 – 5 m) with 50mm lens |
| Flash metering* | TTL metering. Pre-flash used depending on the camera. |
| Ratio flash* | 2:1 when connected with Program/Maxxum Flash 5600HS (D), 5400xi, 5400HS, or 5200i. The lighting ratio set with the connected flash unit. |
| Batteries | Four AA batteries (alkaline, Ni-MH, or lithium) |
| Recycling time and battery performance | Approximate recycling time and number of flashes that can be fired with fresh batteries: Alkaline Ni-MH Lithium Recycling time: 0.2 – 6 seconds 0.2 – 5 seconds 0.2 – 6 seconds Number of flashes: 200 – 4,000 200 – 4,000 500 – 10,000 |
| Dimensions (WxHxD) | 2.56 x 4.53 x 2.72 inches (65 x 115 x 69mm) |
| Weight | 6.7 oz. (190 g) without batteries |
| Standard accessories | Flash case |
| Optional accessories* | Off-Camera Shoe OS-1100, Flash-to-flash Cable CD, Off-Camera Cable OC-1100, Triple Connector TC-1000, Extension Cable EX |

*Compatibility with functions and accessories varies with the camera and lens in use.

Specifications and accessories are subject to change without notice.

#   #   #