Konica Minolta ACTIVA  D WP Binoculars

Specifications

|  | 8x42D WP SPORT | 10x42D WP SPORT |
| --- | --- | --- |
| Prism type | Roof prism BaK4 | Roof prism BaK4 |
| Optical coatings Lens surfaces: Prism surfaces: | Fully multi-coated Phase coating Super reflective coating | Fully multi-coated Phase coating Super reflective coating |
| Magnification | 8x | 10x |
| Objective diameter | 42mm | 42mm |
| Angle of view | 6.7º | 6.1º |
| Apparent angle of view | 53.6º | 61º |
| Exit pupil | 5.3mm | 4.2mm |
| Eye relief | 22mm (long) | 16mm (long) |
| Brightness | 27.6 | 17.6 |
| Field at 1000 yards (Field at 1000m) | 351 ft. (117m) | 320 ft. (107m) |
| Minimum focus distance | 6.6 ft. (2m) | 6.6 ft. (2m) |
| Interpupillary range | 56 - 76mm | 56 - 76mm |
| Dimensions (WxHxD) | 5 x 6.1 x 2 in. (127 x 154 x 51mm ) | 5 x 5.9 x 2 in. (127 x 151 x 51mm) |
| Weight | 22.8 oz. (645g) | 22.6 oz. (640g) |

Specifications are subject to change without notice.

#   #   #

Konica Minolta and Activa are trademarks or registered trademarks of Konica Minolta Co., Ltd.

All other brand and product names are trademarks or registered trademarks of their respective owners.