Konica Minolta DiMAGE Z10 Digital Camera

Specifications

| Number of effective pixels | 3.2 million |
| --- | --- |
| CCD | 1/2.5-type interline primary-color CCD Total pixels: 3.3 million |
| Camera sensitivity | Auto and 64,100, 200, and 400 ISO equivalents |
| Focal length | 6 - 48mm (35mm equivalent: 36 – 290mm) |
| Lens construction | 11 elements in 9 groups |
| Maximum aperture | f/3.2 – f/3.4 |
| Minimum focus distance | Wide: 1.6 ft (0.5m) from front of lens Telephoto: 4.9 ft (1.5m) from front of lens Wide: 1.9 ft (0.57m) from CCD Telephoto: 5.1 ft (1.57m) from CCD |
| Minimum macro distance | Macro Mode: Wide: 0.4 in. (0.01m) Tele: 23.6 in. (0.6m) |
| Maximum magnification | 0.24x Equivalent to 1.5x in 35mm format |
| Area covered at maximum magnification | Approximately 1.0 x 0.7 in. (25 x 18mm) |
| LCD monitor | 1.5 inch (3.8cm) low-temperature polysilicon TFT color Total number of pixels: 113,000 Automatic monitor amplification |
| Field of view | Viewfinder: Approximately 98% LCD monitor: Approximately 100% |
| Display-mode switch | Viewfinder display, LCD-monitor display Switch Finder system allows the monitor to be viewed directly or through the viewfinder. |
| Diopter control | – 3 ~ +1m-1 |
| Eye relief | 18.8mm |
| Shutter | CCD electronic shutter and mechanical shutter |
| Shutter speed range | 4 - 1/2000 second in programmed AE and aperture -priority modes. 15 - 1/2000 second in shutter-priority and manual exposure modes, time exposure (maximum 30 seconds) 2 - 1/2000 second in Auto-recording and Digital Subject Programs |
| Autofocus system | Rapid AF: a combination of a passive AF sensor with the video AF system |
| Autofocus areas | 3-Point Wide Focus Area Spot focus areas with Focus Area Selection |
| Focus modes | Single-shot AF, Continuous AF with predictive focus control, Full-time AF, Manual focus. |
| Focus lock | By pressing shutter-release button partway down. |
| Metering | Multi-segment, Center-weighted, Spot |
| Multi-segment metering | 256 segments |
| Exposure modes | Programmed AE, Aperture priority, Shutter priority, Manual |
| Digital Subject Programs | Automatic (Portrait, Sports action, Landscape, Sunset, Standard) Manual (Portrait, Sports action, Landscape, Sunset, Standard, Night portrait.) |
| Exposure compensation | ±2 EV in 1/3 stop increments |
| AE lock | By pressing shutter-release button partway down |
| Flash metering | Pre-flash TTL |
| Flash range | Wide: Approximately1.6 – 17.1 ft. (0.5 – 5.2 m) from front of lens Telephoto: Approximately 14.9 – 17.1 ft. (.5 – 5.2 m) from front of lens (Camera sensitivity: auto) |
| Flash modes | Autoflash, Autoflash with red-eye reduction, Fill flash, Flash cancel, Slow-shutter sync. Autoflash not available with aperture priority, shutter priority, and manual exposure modes. |
| Flash recycling time | Approximately 4 seconds |
| Flash compensation | ± 2 EV in 1/3 increments |
| Flash-sync speeds | All shutter speeds |
| Continuous advance | Approximately 1.5 frames per second *Actual speed may vary depending upon the subject and camera settings. Approximate number of frames that can be captured at one time with the continuous-advance drive modes: |
|  | Continuous advance |
|  |  | 2048x1536 | 1600x1200 | 1280x960 | 640x480 |
|  | Fine | 5 frames | 8 frames | 13 frames | 42 frames |
|  | Standard | 10 frames | 16 frames | 24 frames | 67 frames |
|  | Economy | 19 frames | 30 frames | 42 frames | 94 frames |
|  | * Actual number of images may vary depending upon the subject and camera settings. |
| Progressive Capture | Stores images from the built-in memory to the memory card from the latest frame captured with the continuous advance. Maximum number of images that can be recorded with the Progressive Capture mode: 6 frames (1.5 frames per second) |
| Exposure bracketing | Three frame bracket in 1.0, 0.5, 0.3 EV increments |
| Self-timer | Approximately 10 seconds , 2 seconds |
| Movie | Recording time dependent on memory card capacity, image size, and frame rate. Frame rate: 15 frames per second (640 x 320, 320 x 240), 30 frames per second (320 x 240) Movie frame capture Night movie (automatic selection or disabled) |
| White balance control | Automatic, Preset (Daylight, Cloudy, Tungsten, Fluorescent, Flash), Custom |

| Digital Effects control | Contrast compensation, Sharpness |
| --- | --- |
| Contrast compensation | Three levels (Low, Normal, High) |
| Sharpness settings | Three levels (Soft, Normal, Hard) |
| Color modes | Natural Color, Vivid Color, Black and white, Sepia |
| Noise reduction | User selectable dark noise reduction |
| Digital zoom | Maximum 4x in 0.1x increments |
| Copy function | To copy single or multiple images to the same or another memory card. |
| E-mail Copy function | Creates a compressed 640 x 480 JPEG image for transmission. |
| Date imprinting | Year/month/day (Format can be changed.) Imprinting can be disabled |
| Key customization | The function activated by the flash-mode button can be changed. |
| Image-quality modes | Fine, Standard, Economy |
| Number of recorded pixels (Still images) | 2048 x 1536, 1600 x 1200, 1280 x 960, 640 x 480 |
| Number of recorded pixels (Movie clips) | 640 x 480, 320 x 240 |
| Storage capacity | Approximate storage capacity of a 16MB SD (Secure Digital) Memory Card: |
|  | Still images |
|  |  | 2048x1536 | 1600x1200 | 1280x960 | 640x480 |
|  | Fine | 9 frames | 14 frames | 22 frames | 69 frames |
|  | Standard | 17 frames | 27 frames | 39 frames | 100 frames |
|  | Economy | 32 frames | 47 frames | 69 frames | 150 frames |
|  | Movie clips |
|  |  | 640 x 480 | 320 x 240 |
|  | 30 frames per second | - | 21 seconds |
|  | 15 frames per second | 26 seconds | 42 seconds |
|  | * Actual number of images may vary depending upon the subject and memory card used. |
| File formats | JPEG, Motion JPEG (MOV) DCF 2.0-compliant DPOF-compliant (Supported by printing functions in version 1.1) Exif 2.2 |
| Folder name formats | Standard, Date |
| Printing output control | Exif Print, PRINT Image Matching II, PictBridge |
| Recording media | SD (Secure Digital) Memory Cards, MultiMediaCards |
| Computer interface | Full-speed 12Mbps data transfer with USB 2.0 compatible computer |
| AV output | NTSC, PAL (selected on the camera) |
| Batteries | Four AA batteries: Alkaline, Ni-MH |
| Battery performance (Playback) | Approximate continuous playback time: 600 minutes with alkaline batteries. |
| Battery performance (Recording) | Approximate number of recorded images: 500 Conforming to CIPA ( included AA alkaline batteries, included SD memory card ) |
| External power source | 6V DC with specified AC adapter (sold separately) |

| Dimensions (WxHxD) | 4.3 x 3.2 x 3.7 in. (109 x 82 x 94mm) |
| --- | --- |
| Weight | Approximately 10.6 oz. (300g) without batteries or recording media |
| Operating temperature | 32-104°F (0-40ºC) |
| Standard accessories | Neck Strap NS-DG800, Lens Cap LF-243B, Video Cable VC-400, 16MB SD (Secure Digital) Memory Card, USB Cable USB-3, DiMAGE Viewer CD-ROM, Four AA Alkaline batteries |
| Optional accessories | AC Adapter AC-1L, Camera Case CS-DG1000, Neck Strap NS- DG7000, Wide-Angle Converter ZCW-200 kit |

System Requirements

IBM PC/AT compatible computers with Windows XP Home, Windows XP Professional,

Windows Me, Windows 2000 Professional, Windows 98*, or Windows 98 Second Edition* and

with a USB port as standard interface.

Apple Macintosh computers with pre-installed Mac OS 9.0 – 9.2.2, Mac OS X v10.1.3 – 10.1.5, and v10.2.1 – 10.2.8, v10.3-10.3.3 and with a USB port as standard interface.

• The computer and operating system must be guaranteed by their manufacturers to support USB interface.

• Problems may be encountered depending on what other USB devices are being used in parallel with this product.

• Only a built-in USB port is supported. Problems may be encountered when the camera is connected to a USB hub.

• Normal operation may not be possible even when all the system requirements are met.

* Users with Windows 98 and Windows 98 Second Edition must install dedicated driver software included in the DiMAGE Z10 package.

#   #   #

Specifications, accessories and system requirements are subject to change without notice.

DiMAGE, CxProcess are trademarks or registered trademarks of Konica Minolta Photo Imaging, Inc.

Windows is either a registered trademark or a trademark of Microsoft Corporation in the United States and/or other countries. Macintosh is a trademark or registered trademark of Apple Computer Inc. Other corporate names and product names are trademarks or registered trademarks of their respective companies.