Konica Minolta DiMAGE Z3 Digital Camera

Specifications

| Number of effective pixels | 4.0 million |
| --- | --- |
| CCD | 1/2.5-type interline primary-color CCD Total pixels: 4.2 million |
| Camera sensitivity | Auto and 50,100, 200, and 400 ISO equivalents |
| Focal length | 5.83 – 69.9mm (35mm equivalent: 35 – 420mm) |
| Lens construction | 13 elements in 10 groups |
| Maximum aperture | f/2.8 – f/4.5 |
| Minimum focus distance | Wide: 2.0ft (0.6m) from front of lens Telephoto: 6.6ft (2.0m) from front of lens Wide: 2.2ft (0.685m) from CCD Telephoto: 6.8ft (2.085m) from CCD |
| Minimum macro distance |  | Super Macro | Standard macro |
|  | Focal length | 10.45mm* | Wide | Telephoto |
|  | From front of lens | 0.4 in. (1 cm) | 3.9 in (10cm) | 47.2 in (120cm) |
|  | From CCD | 3.7 in. (9.5cm) | 7.3 in (18.5cm) | 50.6 in. (128.5cm) |
|  | * at 10.45 mm only |
| Maximum magnification | 0.20x (Equivalent to 1.2x in 35mm format) |
| Area covered at maximum magnification | 1.2 x 0.9 in. (31 x 23mm) |
| Viewfinder type | Electronic viewfinder 0.3-type with a total of 118,000 pixels |
| LCD monitor | 1.5 inch (3.8cm) digital-interface TFT color Total number of pixels: Approximately 78,000 Automatic monitor amplification |
| Field of view | Viewfinder: Approximately 100% LCD monitor: Approximately 100% |
| Diopter control | – 3 ~ +1m-1 |
| Eye relief | 20.8mm |
| Shutter | CCD electronic shutter and mechanical shutter |
| Shutter speed range | 4 - 1/1000 second in programmed-AE and aperture-priority modes. 15 - 1/1000 second in shutter-priority and manual exposure modes. Bulb (maximum 30 seconds) 2 - 1/1000 seconds in auto-recording and Digital Subject Programs |
| Autofocus system | Video AF system |
| Autofocus areas | 5-Point Wide Focus Area Spot focus areas with Focus Area Selection |
| Focus modes | Single-shot AF, Continuous AF with predictive focus control, Full-time AF, Manual focus. |
| Focus lock | By pressing shutter-release button partway down. |
| Metering | Multi-segment, Center-weighted, Spot |
| Multi-segment metering | 256 segments |
| Exposure modes | Programmed AE, Aperture priority, Shutter priority, Manual |
| Digital Subject Programs | Automatic (Portrait, Sports action, Landscape, Sunset, Standard) Manual (Portrait, Sports action, Landscape, Sunset, Standard, Night portrait.) |
| Exposure compensation | ±2 EV in 1/3 increments |
| AE lock | By pressing shutter-release button partway down |
| Flash metering | Pre-flash TTL |
| Flash range | Wide: Approximately 0.7 – 13.1 ft. (0.2 – 4.0 m) from front of lens Telephoto: Approximately 3.9 – 8.2 ft. (1.2 – 2.5 m) from front of lens (Camera sensitivity: auto) |
| Flash modes | Autoflash, Autoflash with red-eye reduction, Fill flash, Slow shutter sync. Autoflash not available with aperture priority, shutter priority, and manual exposure modes. Flash cancel by pushing the built-in flash down. |
| Flash recycling time | Approximately 7 seconds |
| Flash compensation | ± 2 EV in 1/3 increments |
| Flash-sync speeds | All shutter speeds |
| External flashes | Auto-flash metering with Program/Maxxum Flash 2500 (D), Program/Maxxum 3600HS (D), Program/Maxxum Flash 5600HS (D) |

| Continuous advance | - UHS (Ultra High Speed) continuous advance: Approximately 10 frames per second (1280 x 960 ) - Standard continuous advance: Approximately 2.5 frames per second (2272 x 1704) * Actual speed may vary depending upon the subject and camera settings. Approximate number of frames that can be captured at one time with the continuous-advance drive modes: |
| --- | --- |
|  | UHS continuous advance |
|  | 1280x960 |
|  | Fine | 15 frames |
|  | Standard |  |
|  | Economy |  |
|  | Standard continuous advance |
|  |  | 2272x1704 | 1600x1200 | 1280x960 | 640x480 |
|  | Fine | 2 frames | 5 frames | 11 frames | 60 frames |
|  | Standard | 5 frames | 6 frames | 50 frames | 97 frames |
|  | Economy | 5 frames | 51 frames | 72 frames | 115 frames |
|  | * Actual number of images may vary depending upon the subject and camera settings. |
| Progressive Capture | Maximum number of images that can be recorded with the Progressive Capture mode: UHS: 15 frames (10 frames per second) Standard: 5 frames (2.5 frames per second-2272 x 1704, Standard) |
| Exposure bracketing | Three frame bracket in 1.0, 0.5, 0.3 EV increments |
| Self-timer | Approximately 10 seconds, 2 seconds |
| Movie | Recording time dependent on memory card capacity, image size, and frame rate. Frame rate: 15 frames per second, 30 frames per second Audio: monaural Optical zoom is ON in recording Movie frame capture Night movie (automatic selection or disabled) |
| White balance control | Automatic, Preset (Daylight, Cloudy, Tungsten, Fluorescent, Flash), Custom |
| Digital Effects Control | Contrast compensation, Sharpness |
| Contrast compensation | Three levels (Low, Normal, High) |
| Sharpness settings | Three levels (Soft, Normal, Hard) |
| Color modes | Natural Color, Vivid Color, Black and white, Sepia |
| Noise reduction | User selectable dark noise reduction |
| Digital zoom | Maximum 4x in 0.2x increments |
| Copy function | To copy single or multiple images to the same or another memory card. |
| E-mail Copy function | Creates a compressed 640x480 JPEG image for transmission. |
| Date imprinting | Year/month/day (Format can be changed.) Imprinting can be disabled |
| Key customization | The function activated by the flash-mode button can be changed. |
| Image-quality modes | Fine, Standard, Economy |
| Number of recorded pixels (Still images) | 2272 x 1704, 1600 x 1200, 1280 x 960, 640 x 480 1280 x 960 in UHS continuous-advance mode |
| Number of recorded pixels (Movie clips) | 640 x 480, 320 x 240 |

| Storage capacity | Approximate storage capacity of a 16MB SD (Secure Digital) Memory Card: |
| --- | --- |
|  | Still images |
|  |  | 2272x1704 | 1600x1200 | 1280x960 | 640x480 |
|  | Fine | 6 frames | 14 frames | 23 frames | 50 frames |
|  | Standard | 14 frames | 23 frames | 38 frames | 67 frames |
|  | Economy | 27 frames | 41 frames | 53 frames | 100 frames |
|  | Movie clips |
|  |  | 640x480 Fine | 640x480 Standard | 320x240 Standard |
|  | 30 frames per second | 9 seconds | 14 seconds | 30 seconds |
|  | 15 frames per second | 19 seconds | 28 seconds | 58 seconds |
|  | * Movie clips recorded with audio. *Actual number of images may vary depending upon the subject and memory card used. |
| File formats | JPEG, Motion JPEG (MOV): with audio DCF 2.0-compliant DPOF-compliant (Supported by printing functions in version 1.1) Exif 2.2 |
| Folder name formats | Standard, Date |
| Printing output control | Exif Print, PRINT Image Matching II, PictBridge |
| Recording media | SD (Secure Digital) Memory Cards, MultiMediaCards |
| Computer interface | Full-speed 12Mbps data transfer with USB 2.0 compatible computer |
| AV output | NTSC, PAL (selected on the camera) |
| Anti-shake system | CCD-shift Anti-Shake system User selectable |
| Batteries | Four AA batteries: Alkaline, Ni-MH |
| Battery performance (Playback) | Approximate continuous playback time: Approximately 220 minutes with alkaline batteries. |
| Battery performance (Recording) | Approximate number of recorded images: Approximately 170 Conforming to CIPA ( included AA alkaline batteries, included SD memory card ) |
| External power source | 6V DC with specified AC adapter (sold separately) |
| Dimensions (WxHxD) | 4.3 x 3.1 x 3.3 in. (108.5 x 80.0 x 83.5mm) |
| Weight | Approximately 11.8oz (335g) without batteries or recording media |
| Operating temperature | 32-104°F (0-40ºC) |
| Standard accessories | Neck Strap NS-DG7000, Lens Cap LF-243, Accessory Shoe Cap SC-1000, AV Cable AVC-700, 16MB SD (Secure Digital) Memory Card, USB Cable USB-2, DiMAGE Viewer CD-ROM ArcSoft VideoImpression™ 2 CD-ROM (for windows only), Four AA Alkaline batteries |
| Optional accessories | AC Adapter AC-1L, Camera Case CS-DG1000, Wide-Angle Converter ZCW-300 kit, Adapter ring for attaching filter/converter ZCA-300, PROGRAM FLASH 3600HS (D), 5600HS (D), 2500(D) |

System Requirements

IBM PC/AT compatible computers with Windows XP Home, Windows XP Professional, Windows Me, Windows 2000 Professional, Windows 98*, or Windows 98 Second Edition* and with a USB port as standard interface.

Apple Macintosh computers with preinstalled Mac OS 9.0 – 9.2.2, Mac OS X v10.1.3 – 10.1.5, and v10.2.1 – 10.2.8, v10.3-10.3.3 and with a USB port as standard interface.

• The computer and operating system must be guaranteed by their manufacturers to support USB interface.

• Problems may be encountered depending on what other USB devices are being used in parallel with this product.

• Only a built-in USB port is supported. Problems may be encountered when the camera is connected to a USB hub.

• Normal operation may not be possible even when all the system requirements are met.

* Users with Windows 98 and Windows 98 Second Edition must install dedicated driver software included in the DiMAGE Z3 package.

#   #   #

Specifications, accessories and system requirements are subject to change without notice.

DiMAGE, CxProcess are trademarks or registered trademarks of KONICA MINOLTA Photo Imaging, Inc.

Windows is either a registered trademark or a trademark of Microsoft Corporation in the United States and/or other countries. Macintosh is a trademark or registered trademark of Apple Computer Inc. Other corporate names and product names are trademarks or registered trademarks of their respective companies.