Minolta Freedom Zoom 130 35mm Point-and-Shoot Camera

# Specifications

| Camera type | 35mm lens-shutter camera |
| --- | --- |
| Lens | Focal length: 37.5 - 130mm Lens construction: 6 elements in 6 groups (includes two double-sided aspheric elements) Maximum aperture: f/5.4 – f/10.5 Minimum focus distance: Wide: 2 ft. (0.6m) Telephoto: 2.1 ft. (0.65m) |
| Viewfinder | Type: Real-image zoom viewfinder Field of view: 86 % at 9.8 ft. (3m) Magnification: 0.4 - 1.23x Diopter: –1 at 13.1 ft. (4m) |
| Autofocus | Autofocus system: Multi-beam AF (Active AF system) Focusing steps: 2,049 |
| Autoexposure | Metering: Center-weighted Control: Programmed AE Metering range (ISO 100): Wide: EV 3 – 17; Telephoto: EV 3.6 - 17 Exposure compensation: + 1.5 EV Shutter speeds: 10 - 1/380 seconds ISO setting: Automatic with DX-coded film between ISO 25 - 3200 in 1 EV Increments (ISO 25 with non-DX-coded film) |
| Film transport | Automatic loading, Automatic rewind, Manual rewind, Silent rewind |
| Film chamber lock | Yes |
| Flash | Control: Electronic flashmatic Range: With ISO 100 film: Wide: 2 – 14.1 ft. (0.6 – 4.3m); Telephoto: 2.1 – 6.9 ft. (0.65 – 2.1m) With ISO 400 film: Wide: 2 – 28.2 ft. (0.6 – 8.6m); Telephoto: 2.1 – 14.1 ft. (0.65 - 4.3m) * with color negative film Flash modes: Autoflash (in low-light), Autoflash with red-eye reduction, Fill- flash, Flash cancel, Night portrait, Landscape/night view, Exposure compensation Recycling time: Approximately 6.5 seconds |
| Self-timer | 10 seconds |
| Remote control | Date model only IR Remote Control RC-3 (sold separately) |
| Date imprinting | Date model only Year/month/day (Format can be changed.) Day/hour/minute Imprinting can be disabled. |
| Power | Battery: One 3V CR123A lithium battery Battery performance: Twelve 24-exposure rolls (approx.) Based on Minolta's standard test method: flash used with 50% of the exposures with a fresh battery |
| Dimensions (WxHxD) | 4.4 x 2.4 x 1.7 inches (112 x 60 x 44 mm) |
| Weight | 7.4 oz. (210g) |

Specifications are subject to change without notice.

Please see the www.minoltausa.com website for the most updated specifications.

#   #   #