## Minolta Freedom Zoom 140 35mm Camera

## Specifications

| Camera type | 35mm lens-shutter camera |
| --- | --- |
| Lens | Focal length: 37.5 – 140mm Construction: 6 elements in 6 groups (includes 2 double-sided aspheric elements) Maximum aperture: f/5.4 – f/11.7 Minimum focus distance: Wide: 2 ft. (0.6m) Telephoto: 2.6 ft. (0.8m) |
| Viewfinder | Type: Real-image zoom viewfinder (with focus-area illumination by superimposition) Field of view: 85% at 9.8 ft. (3m) Magnification: 0.38 – 1.35 x Diopter: –1 at 16.4 ft. (5m) |
| Eye-start automation | Activates continuous AF and continuous AE |
| Autofocus | Autofocus system: External, passive AF Autofocus sensor: CCD multi-line sensor (7 lines) Focusing steps: 942 Autofocus modes: Wide AF, Spot AF, Target AF Predictive focus control: In target AF mode only Focus lock: In wide and spot AF modes only by pressing shutter-release button partway down |
| Autoexposure | Metering: Multi-segment metering employing a maximum of 125- segments Metering cell: CCD multi-line AF sensor Control: Programmed AE Metering range (ISO 100): Wide: EV 3 – 17; Telephoto: EV 3.9 – 17 AE lock: Exposure is locked with focus by pressing the shutter-release button partway down. Shutter speeds: 10 – 1/500 seconds ISO setting: Automatic with DX-coded film between ISO 25 - 3200 in 1 EV increments (ISO 100 with non-DX-coded film) |
| Film transport | Automatic loading, Automatic rewind, Manual rewind Film chamber lock: Yes |
| Flash | Control: Electronic flashmatic with light intensity control Range: ISO 100: Wide: 2 – 15.1 ft. (0.6 – 4.6 m) Telephoto: 2.6 – 6.9 ft. (0.8 – 2.1 m) ISO 400: Wide: 2 – 30.2 ft. (0.6 – 9.2 m) Telephoto: 2.6 – 13.8 ft. (0.8 – 4.2 m) * with color negative film Flash modes: Autoflash (in low-light, back-light), Autoflash with red-eye reduction (in low-light, back-light), Fill-flash, Flash cancel, Night portrait (with red-eye reduction) Recycling time: 0.5 - 6.5 seconds (approximate) |
| Self-timer | 10 seconds |
| Remote control | Date model only; IR Remote Control RC-3 (sold separately) |
| Date imprinting | Date model only Year/month/day (Format can be changed.) Day/hour/minute Imprinting can be disabled. |
| Power | Battery: One 3V CR123A lithium battery Battery performance: 10 24-exposure rolls (approx.) Based on Minolta's standard test method: flash used with 50% of the exposures with a fresh battery |
| Dimensions (WxHxD) | 4.4 x 2.4 x 1.8 inches (110.5 x 60.5 x 46.5mm) |
| Weight | 6.9 oz. (195 g) without battery |

Specifications are subject to change without notice.

Please see the www.minoltausa.com website for the most updated specifications.

#   #   #